## Slide 1: OpcUaServerWrapper

## Slide 2
OPC UA
Telnet
CN2
Controller
Robot
Server
Client
runs our software

## Slide 3
‘1;1;TIME’
Telnet example (ASCII encoding)
‘QoK04-02-0917:54:32’
‘QeR4220000’
response status
response info
error code
OR

## Slide 4: our software is hosted on a public GitHub repo
git clone https://github.com/Oidlichtnwoada/OpcUaServerWrapper.git

## Slide 5
run at startup
opcua.service
update_repository_and_start_server.sh
1. git pull
OpcUaServerWrapper.git
2. execute Python script
startserver.py

## Slide 6
startserver.py
opcuaserver.py
execute Python script
PC
telnetclient.py
robotcontrollerclient.py
Response
generate Telnet command(s)
Request
return processed controller response
send cmds to controller
receive res from controller
… runs forever …
… communicates with Controller …

## Slide 7: used open-source Python OPC UA library
git clone https://github.com/FreeOpcUa/python-opcua.git

## Slide 8
OPC UA method name | NodeId | Description
ReadInput(Index) | ns=4;i=1067 | reads the input sensor with the corresponding Index
WriteOutput(Index, Value) | ns=4;i=1111 | writes Value to the actuator with the corresponding Index
Move(X,Y,Z,A,B,C) | ns=4;i=1137 | move to position (X,Y,Z) with rotation (A,B,C)
OpenGripper() | ns=4;i=1131 | open the gripper attached to the robot
CloseGripper() | ns=4;i=1134 | close the gripper attached to the robot
GetErrorLog(NumErrorLogs) | ns=4;i=1140 | returns the most recent NumErrorLogs errors
ResetError() | ns=4;i=1108 | resets the current error present in the controller

## Slide 9
Code Walkthrough

## Slide 10
Live Demo